2048
.
SP
RETURN ADDRESS
Activation Record of the CALLEE function
These values are pushed to the stack when CALLEE is invoked from CALLER
RETURN VALUE
ARGUMENT_1
ARGUMENT_n
R0
 .
 .
Rk
BP
OLD BP
Activation Record of the CALLER function
Local Variables of the
CALLER function
1536

---
2047
R2
return addr 76
return value 1
Arg = 1
R1
f
f = 2x1
Old BP 2
return addr 150
return value
return value 2
Arg = 2
result
result = 2
n = 2
Old BP
o) After popping out the return value, the argument and backed up registers. Value of f is computed. return value is stored as 2.
q) RET transfers control to the return addr 150. The return value 2 is stored in register R1.
p) Just before RET instruction in the callee. Local variables are popped and BP is reset to Old BP 2
r) Result is computed. It is same as the return value of fact(). It is then printed, and program exits.
n) The RET instruction obtains return addr from the stack and transfers control back to this address. The return value is stored in R2.
m) Just before the RET instruction, local variables are popped out and BP is reset to OLD BP 3

---
1535
n
BP, SP
BP,SP
e) Just before CALL instruction, registers and arguments are pushed. Space for return value is allocated.
f) CALL instruction pushes the return address of the next instruction 150 to the stack (See machine code)
b) BP is pushed to the stack and BP now points to SP. This shows the starting of activation record of main()
c) Space for local variables n and result of main() are allocated in the stack.
d) The value of n is taken as input from the user and stored in the stack. (Assumed to be 2)
a) BP and SP are initialized as 1535.
f = 1
Old BP 3
Old BP 3
j) CALL pushes the return address 76 to the stack and transfers control to fact()..
k) Control is transferred to fact() again. Old value of BP is backed up. Space for local variable f allocated.
j) CALL pushes the return address 76 to the stack and transfers control to fact()..
i) Just before the recursive call to fact(). Used registers and Argument n-1 is pushed, and space for return value is allocated.
g) Control is transferred to fact(). Old value of BP is backed up. Starting the activation record of fact().
l) Gets into the if condition (base case) and sets f = 1. Stores return value with 1.
h) Space for the local variable f of fact() is allocated in the stack.
o) After popping out the return value, the argument and backed up registers. Value of f is computed. return value is stored as 2.
q) RET transfers control to the return addr 150. The return value 2 is stored in register R1.
p) Just before RET instruction in the callee. Local variables are popped and BP is reset to Old BP 2
r) Result is computed. It is same as the return value of fact(). It is then printed, and program exits.
n) The RET instruction obtains return addr from the stack and transfers control back to this address. The return value is stored in R2.
m) Just before the RET instruction, local variables are popped out and BP is reset to OLD BP 3
BP, SP